## Slide 1
Basic Mobile Lab II
Mobile System Engineering, Dankook University

## Slide 2
1
USB Bridge – ATmega16u2 / CH340
CH340
USB to Serial Converter
Usb data converts to serial communication data
USB
Serial
Notes: 아두이노 우노 - USB to Serial 통신 (tistory.com)

## Slide 3
2
Microcontroller – ATmega328(28 pin DIP(Dual In-Line))
ATMEGA328-PU Datasheet(PDF) - ATMEL Corporation (alldatasheet.com)

## Slide 4
3
Microcontroller – ATmega328(28 pin MLF(Micro LeadFrame))
Features
High performance, Low power AVR® 8-Bit Microcontroller
Advanced RICS Architecture
High Endurance Non-volatile Memory Segments
32K Bytes of In-system self-programmable Flash program memory
1K Bytes EEPROM
2K Bytes Internal SRAM
Peripheral Features
6 PWM channels
6-channel 10-bit ADC
Programmable Serial UART
Master/Slave SPI Serial Interface
Byte-oriented 2-wire Serial Interface(I2C)
I/O and Packages
23 Programmable I/O Lines
Operating Voltage
1.8V~5.5V for ATmega328P
Temperature Range: -40°C to 85°C

## Slide 5
Arduino Communication method
2

## Slide 6
1
Arduino Communication method
Classification according to data transmission method
Simplex
Half Duplex
Full Duplex

## Slide 7
2
Arduino Communication method
Serial Interface
OUT
CLK
IN
CLK
b0
b1
b2
b3
b4
b5
b6
b7
1). Synchronous Serial
Data is sent in a continuous stream at constant rate. The clocks in the transmitting and receiving devices are synchronized. No start or stop bits are required.
OUT
IN
b0
b1
b2
b3
b4
b5
b6
b7
2). Asynchronous Serial
Instead of a common synchronization signal, the data stream contains synchronization information in form of start and stop signals, before and after each unit of transmission, respectively.
b8
b9
Start
End
Pros: fewer lines required for communication
Cons: slow communication(require start and end signals to indicate)
Pros: fast communication
Cons: master and slave structure
Notes: 시리얼 통신 기초 (Serial Communication) | Hard Copy World

## Slide 8
3
Arduino Communication method
1. Serial(UART, Universal Asyncronous Receiver/Transmitter)
Asyncronous
It communicates by converting data, processed at once in parallel into a data stream serially
1(High) -> 3.3V, 0(Low) -> 0~0.8V
Simple method, low cost, easy to implement, but low speed and throughout.
Arduino serial communication pin(UNO): D0(RX-Receive), D1(TX-Transmit)

## Slide 9
4
Arduino Communication method
1. Serial(UART, Universal Asyncronous Receiver/Transmitter)
Baudrate: data rate transmitted over serial line.
- Unit[bps] -> bit per second
- EX) 9600[bps] -> 9600bits per 1 second
Frame of the data
- data packet
Start
Data
Parity
Stop
Frame:
Size(bits):
1
5-9
0 or 1
1-2
Notes: 시리얼 통신 기초 (Serial Communication) | Hard Copy World

## Slide 10
5
Arduino Communication method
1. Serial(UART, Universal Asyncronous Receiver/Transmitter)
Frame of the data
- Parity bit(Check bit): A bit added to a string if binary code. Simple form of error detecting code. It ensures that the total number of 1-bits in the string is even or odd. Optional bit.
Transmit 120 in 8bit
0
1
1
1
1
0
0
0
0
?
1
1
1
0
0
0
Receive 56 in 8bit
ERROR – Wrong data
Total number of 1 bits -> 4 -> even
1
1
1
1
0
0
0
0
?
1
1
1
0
0
0
0
Can predict the total number of 1bits was an even number
* Apply even parity
1
1
1
1
0
0
0
0
Receive 120 in 8bit
Notes: 코끼리를 냉장고에 넣는 방법 :: [개념정리] 패리티 비트(Parity Bit)란? (tistory.com)

## Slide 11
6
UART Experiment
GND -> Probe GND
TX -> Probe hook

## Slide 12
7
UART Experiment
Text -> ASCII -> Binary
ASCII, 10진수, 16진수, 8진수, 2진수 변환표 - IBM Documentation

## Slide 13
8
UART Experiment
0100000101
Text -> ASCII decimal-> Binary
A -> 65 ->1000001
End signal
Start signal

## Slide 14
9
Arduino Communication method
2. SPI(Serial Peripheral Interface)
Synchronous
A protocol for multiple slave devices to commiunicate with one master devices. -> 1:N
Use 4 lines for communication
Full duplex (Clock: SCL)
SCK
MOSI
MISO
SS
SCK
MOSI
MISO
SS
SLAVE 1
SLAVE n
MASTER
SCK
MOSI
MISO
SS1
SSn
 | description
SCK | Serial clock
MOSI | Master output / Slave input
MISO | Master input / Slave output
SS | Slave select

## Slide 15
10
Arduino Communication method
2. SPI(Serial Peripheral Interface)
SCK
MOSI
MISO
SS
Master to Slave
Slave to Master
0
1
2
3
4
5
6
7
1
1
0
0
1
0
1
0
0
1
2
3
4
5
6
7
0
1
1
0
0
0
1
0
ASCII ‘F’
ASCII ‘S’
End after last byte sent or received

## Slide 16
11
Arduino Communication method
3. I2C(Inter-Integrated Circuit) or TWI(Two Wire Interface)
Synchronous
A protocol for multiple slave devices to commiunicate with multiple master devices. -> N:N
Use 2 lines for communication
Half duplex (Clock: SCL)
SDA
SCL
Device1
(Master)
Device2
(Slave)
Device3
(Slave)
Device N
(Slave)
R1
R2
…
Pull-up resistor

## Slide 17
12
Arduino Communication method
3. I2C(Inter-Integrated Circuit) or TWI(Two Wire Interface)
Frame of the data
Slave Address: To indicate which salve the data transmitted by the master goes to.
Data: data to transmit.
SDA
SCL
…
…
1
2
7
8
9
2
1
8
9
Slave Address
Data (Master)
start
stop
7 addreses bits
8 data bits
Ack bit
Ack bit
Write bit
SDA goes low before SCL
SDA goes high after SCL
Write(0) – master is sending data
Read(1) – mater is requesting data
ACK(0)/NACK(1): ‘1’ indicates that the addressed slave did not respond or was unable to process the request. This bit controls by slave device.
Example of write data to slave device

## Slide 18
13
Arduino Communication method
 | UART | I2C | SPI
Type | Asynchronous | synchronous | synchronous
Topology | 1:1 | N:N | 1:N
Signal lines | Rx, Tx | SDA, SCL | SCK, MISO, MOSI, SS
Duplex | Full | Half | Full
Speed | slow -> fast |  | fast

## Slide 19
14
Arduino Communication method
4. Software serial
If D0 and D1 pins are already being used for communication, you can use the other digital pins to use the software serial library.
11
10
5V
GND
VCC
GND
TXD
RXD
10 pin -> RXD 11 pin -> TXD GND -> GND 5V -> VCC

## Slide 20
15
Arduino Communication method
4. Software serial
If D0 and D1 pins are already being used for communication, you can use the other digital pins to use the software serial library.

## Slide 21
1
Bluetooth

## Slide 22
2
Bluetooth
Bluetooth
A short range wireless technology(~10[m])
use for exchanging data between fixed and mobile devices over short distance and building personal area networks(PAN).
It uses UHF(Ultra High Frequency) radio waves
in the ISM(Industry-Science-Medical) bands, from
2402~2480[MHz].
Master
Slave
Computer network types by spatial scope
Bluetooth
Zigbee
NFC(Near Field Communication)
Class | power[mW] | distance[m]
Class1 | 100 | 100
Class2 | 2.5 | 10
Class3 | 1 | 1
Class4 | 0.5 | 
Bluetooth device power and distance by class
ISM bands
Notes: Data Networks classification by spatial scope - 개인 통신망 - 위키백과, 우리 모두의 백과사전 (wikipedia.org)

## Slide 23
3
Bluetooth
Pros
avoid interference from other wireless devices
low power consumption
cheap cost
can connect through any obstacles
Cons
low bandwitdth compare to Wi-fi
short range communication between devices
weak security

## Slide 24
4
Bluetooth
Bluetooth principle
master, slave communication
M
S
M
S
S
S
M
S
S
S
M
M
S
S
Single Slave Piconet
Multi-Slave Piconet
Scatternet

## Slide 25
5
Bluetooth
Bluetooth principle
BT uses a frequency-hopping spread spectrum(FHSS) method to prevent interference between radio waves because it uses the same frequency in many devices.
The frequency of a BT radio is changed by frequency hops between ISM band channels.
79 channels, 1[MHz] bandwidth, maximum hop rate 1600[Hz](=625us)

## Slide 26
5
Bluetooth
Bluetooth principle

## Slide 27
MIT APP INVENTOR

## Slide 28
search MIT APP INVENTOR on Google
MIT APP INVENTOR select
3
MIT APP INVENTOR

## Slide 29
3. Create Apps! to create your account
3
MIT APP INVENTOR

## Slide 30
4. New project -> project name
3
MIT APP INVENTOR

## Slide 31
5. layout -> drag and drop 3 Horizontal Arrangement
3
MIT APP INVENTOR

## Slide 32
6. select Horizontal Arrangement 1,2 -> height: automatic, width: fill parents
7. select Horizontal Arrangement 3 -> height: fill parents, width: fill parents
3
MIT APP INVENTOR

## Slide 33
User interface
Horizontal Arrangement 1 -> add list picker , Horizontal Arrangement 2 -> add 3 labels
3
MIT APP INVENTOR

## Slide 34
List picker 1
Font size -> 25, Width -> fill parent, Text -> Bluetooth connect
3
MIT APP INVENTOR

## Slide 35
label 1,2,3
Font size -> 25, Width -> 33%, Text -> ECG, 0, V(label 1,2,3)
3
MIT APP INVENTOR

## Slide 36
drawing & animation (canvas) -> add to horiziontal arrangement
Extend Moves Outside Canvas check, height & width -> fill parent
3
MIT APP INVENTOR

## Slide 37
insert sensor(clock)
time interval -> 100
3
MIT APP INVENTOR

## Slide 38
connecivity (Bluetooth client) add
3
MIT APP INVENTOR

## Slide 39
select blocks
3
MIT APP INVENTOR

## Slide 40
bulit-in (variables) -> nitialize global
bulit-in (math) -> 0
3
MIT APP INVENTOR

## Slide 41
list picker 1 -> when list picker 1 beforepicking/afterpicking do
3
MIT APP INVENTOR

## Slide 42
list picker 1 -> set list picker 1 elements to/selection to
3
MIT APP INVENTOR

## Slide 43
bluetooth client 1 -> bluetooth client 1 addresss and names, call bluetooth client1 connect address
list picker 1 -> list picker 1 selection
3
MIT APP INVENTOR

## Slide 44
control -> if then else if then else
clock 1 -> set clock 1 timer enabled to
3
MIT APP INVENTOR

## Slide 45
bluetooth -> bluetooth client 1 is connected
logic -> true, not, false
3
MIT APP INVENTOR

## Slide 46
clock 1 -> when clock1 timer do
control -> if then
bluetooth 1 -> bluetooth client 1 is connected
3
MIT APP INVENTOR

## Slide 47
variables -> set global X_before to get global X
-> set global Y_before to get global Y
-> set global X to
-> set global Y to
3
MIT APP INVENTOR

## Slide 48
math -> □ + □ -> get global X_before-> 15
bluetooth client 1 -> call bluetooth client1 receivetext number of bytes, call bluetooth cluent 1 bytes available to receive
3
MIT APP INVENTOR

## Slide 49
label 2 -> set label 2 text to
text -> segment text start length
3
MIT APP INVENTOR

## Slide 50
variables -> get global Y
math -> 1, 5
3
MIT APP INVENTOR

## Slide 51
canvas 1 -> call canvas1 drawline
variables -> get global Y before, get global X
3
MIT APP INVENTOR

## Slide 52
math -> □ - □
canvas 1 -> canvas1 height
3
MIT APP INVENTOR

## Slide 53
math -> □ X □
math -> 500
variables ->> get global X before, get global Y_before
3
MIT APP INVENTOR

## Slide 54
control -> if then
math -> □ = □ -> □ ≥ □
3
MIT APP INVENTOR

## Slide 55
variables -> get global X
canvas1 -> canvas1 width
3
MIT APP INVENTOR

## Slide 56
canvas1 -> call canvas1 clear
variables -> set global X_before to, get global X to
3
MIT APP INVENTOR

## Slide 57
math -> 0
3
MIT APP INVENTOR

## Slide 58
build -> Android App
3
MIT APP INVENTOR

## Slide 59
3
MIT APP INVENTOR

## Slide 60
Google Play Store -> MIT A12 Companion
MIT A12 Companion -> Scan QR code
3
MIT APP INVENTOR

## Slide 61
1
Bluetooth AT command

## Slide 62
2
Bluetooth AT command
HC-06 AT commands
To check connection, send ’AT’, and you should get ‘OK’ back.
Send: AT
To check HC-06 version.
Send: AT+VERSION
To check HC-06 address.
Send: AT+ADDR
To set the device name send below command.
Send: AT+NAMEDEVICE01
To set the Bluetooth password.
Send: AT+PSWD1234
To set the baudrate send the below command, where ‘X’ is a number corresponding to the baudrate.
Send: AT+BAUD2
AT+BAUDX | Baudrate
1 | 1200
2 | 2400
3 | 4800
4 | 9600(default)
5 | 19200
6 | 38400
7 | 57600
8 | 115200
9 | 230400
A | 460800
B | 921600
C | 1382400

## Slide 63
Thank You Thanks Gratitude - Free image on Pixabay